## Slide 1: Principles of Compiler Construction
© Copyright 2008-2010, Sun Yat-sen University
Lecturer: CHANG HUIYOU
Note that most of these slides were created by:
Prof. Wen-jun LI
Dr. Zhong-mei SHU Dr. Han LIN

## Slide 2: Lecture 11. Code Generation
Introduction
Abstraction of Target Machines
Implementation of Procedures
Optimization of Basic Blocks
A Simple Code Generator
Peephole Optimization

## Slide 3: 1. Introduction
Code generators focus on
  1. Instruction selection
    Choose appropriate target-machine instructions to implement IR statements.
  2. Register allocation and assignment
    Make full use of registers, the fastest computational unit.
  3. Instruction ordering
    Decide the order in which the execution of instructions is scheduled.
    Also called instruction scheduling.

## Slide 4: Instruction Selection
Both the speed and the size cost of the generated code should be considered.
  Trade-off and consequence.
Example 1: a = a + 1
  LD R0, a ADD R0, R0, #1 ST a, R0
  INC a
Example 2: set register R0 to 0
  LD R0, #0
  XOR R0, R0

## Slide 5: Register Allocation and Assignment
Include two subproblems
  Register allocation
    Select the set of variables that will reside in registers at each point in the program.
  Register assignment
    Pick the specific register that a variable will reside in.
A difficult problem in code generation.

## Slide 6: Instruction Scheduling
Important for modern pipelined processors
  RISC: Reduced Instruction Set Computer
    RISC vs. CISC
  Data Hazards (stalls in a pipeline): attempt to use a datum before it becomes available in register.
    A value written to a register will not be available in its following cycles.
    The following cycles should be utilized by instructions that does not depend on the value
      Or they will be wasted.
    Optimization: clustering instructions with no dependencies together, while preserving original semantics.

## Slide 7: Instruction Scheduling (cont')
An example: (a + b) + c on SGI's MIPS 2000
  LD R1, a LD R2, b NOP ADDi R1, R1, R2 LD R2, c NOP ADDi R1, R1, R2 指令流水线：
Optimal generated code 取指令
  LD R1, a 译码
  LD R2, b 执行 LD R3, c 访存 ADDi R1, R1, R2 写回寄存器堆 NOP ADDi R1, R1, R3

## Slide 8: 2. Abstraction of Target Machines
Instruction set
Addressing modes
Program and instruction costs

## Slide 9: Instruction Set
Supports the following instructions
  LD dst, addr // load
  ST x, Ri // store
  OP dst, src1, src2 // ADD, SUB, ... OP dst, src1 // unary operation
  BR L // branch
  Bcond r, L // conditional branch

## Slide 10: Addressing Modes
Addressing in instructions
  #C // immediate constant, cost = 1
  x // absolute, cost = 1
  *x // indirect memory, cost = 1
  R // direct register, cost = 0
  *R // indirect register, cost = 0
  a(Ri) // direct indexed, cost = 1
    a is a variable or a constant
    LD R1, a(R2)
      R1 = contents(a + contents(R2))
    LD R1, 100(R2)
      R1 = contents(100 + contents(R2))
  *a(Ri) // indirect indexed, cost = 1
    LD R1, *100(R2)
      R1 = contents(contents(100 + contents(R2)))

## Slide 11: Program and Instruction Costs
Cost of an instruction
  = 1 + operand_addr_cost
Cost of a program
  = total of instruction costs
Examples
  LD R0, R1 // cost = 1
  LD R0, x // cost = 2
  LD R1, *100(R2) // cost = 2

## Slide 12: 3. Implementation of Procedures
Static Allocation
Stack Allocation

## Slide 13: Static Allocation
Implementation of call callee
  ... ST callee.staticArea, #here + 20 // return address BR callee.codeArea // jump to Callee ...
Implementation of return
  ... BR *callee.staticArea // return to Caller
Assume that the return address
is saved at the beginning of
the activation record. And
20 = 5 words * 4 bytes/word

## Slide 14: An Example: Three-Address Code
// code for c
action1
call p
action2
halt
// code for p
action3
return

## Slide 15: An Example: Implementation
// code for c
100 action1
120 ST 364, #140 // return address
132 BR 200 // call p
140 action2
160 HALT // return to operating system
...
// code for p
200 action3
220 BR *364 // return to its caller
....
// activation record for c
300 // return address to Caller
304 // local data for c
....
// activation record for p
364 140 // return address to Caller
368 // local data for p

## Slide 16: Stack Allocation
Implementation of initialization
  LD SP, #stackStart // initialize the stack ... // code for main() HALT // terminate
Implementation of call callee
  ... ADD SP, SP, #caller.recordSize // push an AR ST *SP, #here + 16 // return address BR callee.codeArea // jump to Callee SUB SP, SP, #caller.recordSize // pop the AR ...
Implementation of return
  ... BR *0(SP) // return to Caller
DBv2 must assume that addressing 0(SP) has no additional cost

## Slide 17: An Example: Three-Address Code
// code for m
action1
call q
action2
halt
// code for p
action3
return
// code for q
action4
call p
action5
call q
action6
call q
return

## Slide 18: An Example: Implementation
100 LD SP, #600
108 action1
128 ADD SP, SP, #msize
136 ST *SP, #152
144 BR 300
152 SUB SP, SP, #msize
160 action2
180 HALT
...
200 action3
220 BR *0(SP)
....
300 action4
320 ADD SP, SP, #qsize
328 ST *SP, #344
336 BR 200
344 SUB SP, SP, #qsize
352 action5
372 ADD SP, SP, #qsize
380 ST *SP, #396
388 BR 300
396 SUB SP, SP, #qsize
404 action6
424 ADD SP, SP, #qsize
432 ST *SP, #448
440 BR 300
448 SUB SP, SP, #qsize
456 BR *0(SP)
...
600
code for p
code for q
blue for call sequence
stack

## Slide 19: 4. Optimization of Basic Blocks
Approach
Basic Block
DAG
Basic Block
Petri Nets in
Super Compiler

## Slide 20: Basic Blocks
Single entry and single exit
Example
(10) i = i + 1
(11) if i <= 10 goto 2
(12) i = 1
(13) t5 = i – 1
(14) t6 = 88 * t5
(15) a[t6] = 1.0
(16) i = i + 1
(17) if i <= 10 goto 13
(1) i = 1
(2) j = 1
(3) t1 = 10 * i
(4) t2 = t1 + j
(5) t3 = 8 * t2
(6) t4 = t3 – 88
(7) a[t4] = 0.0
(8) j = j + 1
(9) if j <= 10 goto 3

## Slide 21: Flow Graphs
i = 1
t1 = 10 * i
t2 = t1 + j
t3 = 8 * t2
t4 = t3 – 88
a[t4] = 0.0
j = j + 1
if j <= 10 goto B3
j = 1
i = 1
i = i + 1
if i <= 10 goto B2
ENTRY
EXIT
t5 = i – 1
t6 = 88 * t5
a[t6] = 1.0
i = i + 1
if i <= 10 goto B6
B1
B5
B4
B3
B2
B6

## Slide 22: Construction of Flow Graphs
Partition three-address instructions into basic blocks
  Leader: the 1st instruction in a basic block.
  Algorithm to find all leaders
    The 1st three-address instruction
    Target of a conditional or unconditional jump
    Instruction immediately follows a conditional or unconditional jump

## Slide 23: Liveness and Next-Use Information
Calculate liveness and next-use info in a basic block: backward scanning
  Initialize: for each variable v,
    v.nextUse = none; v.liveness = v is temporary ? false : true;
  For each i: x = y + z
    Attach information of x, y and z to instruction i;
    x.liveness = false; x.nextUse = none;
    y.liveness = z.liveness = true; y.nextUse = z.nextUse = i;
Conservative.
Global data-flow analysis in practice

## Slide 24: An Example
Information are stored at the entry of each variables in the symbol table
(1) t = a – b
(2) u = a – c
(3) v = t + u
(4) d = v + u
(1) t(3),T = a(2),T – b – ,T
(2) u(3),T = a – ,T – c – ,T
(3) v(4),T = t – ,F + u(4),T
(4) d – ,T = v – ,F + u – ,F
Var. | Next-Use |  |  |  |  | Liveness |  |  |  | 
 | Init | (4) | (3) | (2) | (1) | Init | (4) | (3) | (2) | (1)
a |  |  |  | (2) | (1) | T |  |  | T | T
b |  |  |  |  | (1) | T |  |  |  | T
c |  |  |  | (2) |  | T |  |  | T | 
d |  |  |  |  |  | T | F |  |  | 
t |  |  | (3) |  |  | F |  | T |  | F
u |  | (4) | (3) |  |  | F | T | T | F | 
v |  | (4) |  |  |  | F | T | F |  | 

## Slide 25: Optimization Based on DAGs
Perform several code-improving transformations
  Elimination of local common subexpressions
  Elimination of dead code
  Reordering of independent statements
  Application of algebraic laws

## Slide 26: Local Common Subexpressions
a = b + c
b = a – d
c = b + c
d = a – d
b0
c0
+
d0
–
+
b, d
c
a
a = b + c
d = a – d
c = d + c
b = d
Only if b is
live on exit

## Slide 27: Dead Code
Suppose only
a and b are
live on exit
a = b + c
b = b – d
c = c + d
e = b + c
a = b + c
b = b – d
b0
c0
+
d0
–
+
b
c
a
+
e
1st
2nd

## Slide 28: Algebraic Identities
Arithmetic identities
  x + 0 = 0 + x = x
  x * 1 = 1 * x = x
  x – 0 = x
  x / 1 = x
  ...
Local reduction in strength
  2 * x  x + x
  x / 2  x * 0.5
  ...
Constant folding
  2 * 3.14  6.28
  ...

## Slide 29: Array References
x = a[i]
a[j] = y
z = a[i]
a0
i0
=[ ]
j0
=[ ]
x
killed
=[ ]
z
y0

## Slide 30: An Example: Construction a DAG from a BB (1)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
4
*
t1
i0

## Slide 31: An Example: Construction a DAG from a BB (2)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
4
*
t1
i0
=[ ]
t2

## Slide 32: An Example: Construction a DAG from a BB (3)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
4
*
t1, t3
i0
=[ ]
t2

## Slide 33: An Example: Construction a DAG from a BB (4)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
i0
t4
=[ ]
t2

## Slide 34: An Example: Construction a DAG from a BB (5)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
t4
t5
=[ ]
t2

## Slide 35: An Example: Construction a DAG from a BB (6)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
t4
t5
=[ ]
t2
+
prod0
t6

## Slide 36: An Example: Construction a DAG from a BB (7)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
t4
t5
=[ ]
t2
+
prod0
t6, prod

## Slide 37: An Example: Construction a DAG from a BB (8)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
1
+
t7
t4
t5
=[ ]
t2
+
prod0
t6, prod

## Slide 38: An Example: Construction a DAG from a BB (9)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
1
+
t7, i
t4
t5
=[ ]
t2
+
prod0
t6, prod

## Slide 39: An Example: Construction a DAG from a BB (10)
t1 = 4 * i
t2 = a[t1]
t3 = 4 * i
t4 = b[t3]
t5 = t2 * t4
t6 = t5 + prod
prod = t6
t7 = i + 1
i = t7
if i <= 20 goto (1)
a0
b0
=[ ]
4
*
t1, t3
*
i0
1
+
t7, i
20
<=
(1)
t4
t5
=[ ]
t2
+
prod0
t6, prod

## Slide 40: 5. A Simple Code Generator
What does "simple" mean ?
  Generate code for a single basic block.
Motivation
  Make full use of registers to the best advantage.
Programmer
Compiler
OS and Hardware
Storage | Access Cycles | Capability
Registers | 1 | 256-8000 Bytes
Cache | 3 | 256 KB - 1 MB
Main memory | 20-100 | 32 MB - 1 GB
Disk | 0.5-5 Mega | 10 GB - 1 TB

## Slide 41: Register and Address Descriptors
Register descriptor
  RegDesc: Register  2Variable
Address descriptor
  AddrDesc: Variable  2Location
  Location = Register  Memory

## Slide 42: Code-Generation Algorithm
Based on function getReg(x = y op z)
  Select registers for variables in three-address instruction x = y op z.
    That is Rx, Ry and Rz for x, y and z respectively.
  Make decisions based on the register descriptor and the address descriptor.

## Slide 43: Code-Generation Algorithm (cont')
Machine instructions for x = y + z
  Call getReg(x = y + z) to select registers Rx, Ry and Rz for x, y and z.
  If y  regDesc(Ry), get some y'  addrDesc(y) and issue an instruction: LD Ry, y'.
  If z  regDesc(Rz), get some z'  addrDesc(z) and issue an instruction: LD Rz, z'.
  Issue an instruction: ADD Rx, Ry, Rz.
  Adjust register and address descriptors.

## Slide 44: Code-Generation Algorithm (cont')
Machine instructions for x = y
  Call getReg(x = y) to select registers Rx and Ry.
    getReg() will always choose the same register for both x and y.
  If y  regDesc(Ry), get some y'  addrDesc(y) and issue an instruction: LD Ry, y'.
  Adjust register descriptor: regDesc(Ry) = {x}

## Slide 45: Design of getReg(...)
Input: x = y + z
Output: Rx, Ry and Rz
Algorithm (use Ry as an example)
  if y in some registers, pick Ry in them.
  elsif there is empty registers, pick one as Ry.
  elsif { let R be a candidate and R holds v, foreach v check:
    if addrDesc(v) has other location, R is OK.
    elsif v == x and x != z, R is OK.
    elsif v is not used later, R is OK.
    else spill, i.e. issue ST v, R.
  choose the R with minimal spills }.

## Slide 46: 6. Peephole Optimization
A simple but effective technique for locally code improvement
  Examine a sliding window (peephole) of target instructions.
  Replace instruction sequence within the peephole by a shorter or faster sequence.

## Slide 47: Eliminating Redundant Loads and Stores
Examples
  LD R0, a ST a, R0 // eliminated

## Slide 48: Eliminating Unreachable Code
Examples
  if debug == 1 goto L1 goto L2 L1: print debugging information L2: if debug != 1 goto L2 print debugging information L2:

## Slide 49: Flow-of-Control Optimizations
Examples
  goto L1 ... L1: goto L2 goto L2 ... L1: goto L2
  if a < b goto L1 ... L1: goto L2 if a < b goto L2 ... L1: goto L2
Recall the translation scheme of
flow-of-control statements !

## Slide 50: Algebraic Simplification and Reduction in Strength
Examples
  x = x + 0 // eliminated
  x = x * 1 // eliminated
  y = x * 2 y = x << 1
  y = x * 4 y = x << 2

## Slide 51: Enjoy the Course!